## Slide 1: Visual Perception and Eyetracking: Eye Movement and its Analysis
Jacek Matulewski
Institute of Physics, NCU
ICNT, UMK
WWW: http://www.fizyka.umk.pl/~jacek
E-mail: jacek@phys.uni.torun.pl
TAPS, 22-08-2018

## Slide 2: Senses
Humans receptors
Vision 250 000 000 photoreceptor cells
Olfaction (smell) 40 000 000 chemoreceptors
Haptics, pain 2 500 000 mechanoreceptors
Taste 1 000 000 chemoreceptors
Hearing 25 000 mechanoreceptors
Receptors are in whole body
Source: http://www.if.pwr.wroc.pl/~wozniak/kolorymetria_pliki/
80% inform. about envir. – vision, 10% cerebral cortex

## Slide 3: Visual perception
Human eye
200,000 photocells / mm2 (average)
90 millions of rod cells (light intensity, night)
4,5 millions of cone cells (color, day vision)
Image source: Wikipedia
Bird of prey (eagle, falcon)
1 milion of photocells / mm2
CCD (lub CMOS)
10 Mpx / cm2 = 0.1 Mpx / mm2

## Slide 4: Visual perception
Source: Holmqvist i in. Eye Tracking. A Comprehensive Guide to Methods and Measures
How many degrees of freedom does the human eye have?

## Slide 5: Purkinje images
Image source: https://ppw.kuleuven.be/home/english/research/lep/images/resources/eye1
Lens
Sclera
Cornea
Iris
incoming ray
P1 - reflection from the outside
corneal surface (glint)
P2 - reflection from the inside
corneal surface
P3 - reflection from the outside
the surface of the lens
P4 - reflection from the inside
the surface of the lens

## Slide 6: Purkinje images
Image source: http://www.eyetracking.com/Hardware/Eye-Trackers

## Slide 7: Eyetracker – hardware
Mirametrix
Image source: http://www.eyetracking.com/Hardware/Eye-Trackers
SMI
SMI
EyeLink
Kamil Pleskot
Remote and
head-mounted
eye trackers

## Slide 8: Eyetracker – DIY hardware
Source: Kamil Pleskot (engineering thesis)
IR diodes
USB cable
ophthalmic
frame (old)
CMOS sensor
(from web cam)

## Slide 9: Eyetracker – DIY hardware
frame of
glasses
CMOS sensor
(from web cam)
IR diodes
Source: Kamil Pleskot (engineering thesis)

## Slide 10: Eyetracker – software
The use of P1 (glint) makes the gaze position detection
independent on the movement of the head
Source: Holmqvist i in. Eye Tracking. A Comprehensive Guide to Methods and Measures

## Slide 11: Eyetracker – software
Glasses make the glint recognition harder
Source: Kamil Pleskot

## Slide 12: Eye movement
Eyes never stop moving.
La saccadé (fr. jolt, jerk, rapid movement)
During wake time – 200,000 saccades. During sleep, the eye movement changes (REM - rapid eye movements).
The small part of the eye movements is controlled consciously (like breathing)
Most of the movements (including the microsaccades) are not controlled and we are not aware of them. Otherwise the image would be constantly shaking.
Even during fixation on the subject the eye is not still!
Microsaccades - movements of the eye with a smaller amplitude "within" the fixation object. The microsaccades are responsible for "refreshing" the image (stimulating the eye rods and cons).
Without it we would see only moving objects (like some animals).
Erasmus Darwin (Charles’ grandfather, 1794): staring at a very small piece of silk on paper - the color gradually fades and disappears!
Susanna Martinez-Conde http://static.trogu.com/documents/articles/palgrave/references/martinez-conde%20vision%20saccades.pdf

## Slide 13: Eye movement
Experiments carried out in the 1950s:
Freeze the image by placing the projector on the contact lens
Effect: the image disappears (perceptually), no stimulation of eye photoreceptors
Roy M. Pritchard Stabilized Images on the Retina (https://pdfs.semanticscholar.org/c97a/209e1a1caa088ae94987fe59317b5ef68838.pdf)
An example of a woman (the only one) with complete paralysis of the eye's muscles (fibrosis): she learn that nerves’ stimulation and thus vision is possible thanks to the head movement. She is even possible to read.
Gilchrist i in. Saccades without eye movements Nature 390 (1997) 130-131

## Slide 14: Eye movement
Experiment of Johna K. Stevensa:
John K. Stevens i in. Paralysis Of The Awake Human: Visual Perceptions Vision Research 16 (1976) https://pdfs.semanticscholar.org/8567/8b73e4f918f05244b66ca2a9f65ef89ed3d9.pdf
JKS is object/observer.
Injection of a neuromuscular-blocking drug (succinylcholine) and curare
A tourniquet on the right hand
prevents its paralysis (communication)
Breathing support (respirator)
Mirror and screen (stimulus)
The total immobilization of the eye
Image fading becomes a problem
Conscious attempts of sakad (effort)
caused the world to move? (despite the lack of changes in the image!)
Conclusion: the perception of space is not
simple function of info. from senses,
but also of planned eye movements (sensory processing / integration)

## Slide 15: Eye movement - Events
The schema does not retain the scale of the real eye movement
fixation
saccade
glisade
fixation
drift
microsaccade

## Slide 16: Eye movement - Events
Zdarzenie | Czas trwania | Długość | Prędkość
Fixation | 200-300 ms | - | -
Saccade | 30-80 ms | 4-20° | 300-500°/s
Glissade (correction after saccade) | 10-40 ms | 0.5-2° | 20-140°/s
Smooth pursuit | - | - | 10-30°/s
Drift (slow move of the gaze position out of the fixation center) | 200-1000 ms | 1-60’ | 6-25’/s
Microsaccade (correction after the drift) | 10-30 ms | 10-40’ | 15-50°/s
Tremor (of eye muscles) | - | < 1’ | < 20’/s

## Slide 17: From exploration to fixation
Źródła: in. i Susanna Martinez-Conde From Exploration to Fixation: An Integrative View of Yarbus’s Vision Perception 44 (2015) 884-899
Jorge Otero-Millan, Stephen L. Macknik, Rachel E. Langston and Susana Martinez-Conde An oculomotor continuum from exploration to fixation PNAS 110 (2013) 6175-6180
As the size of the stimulus decreases
the parameters of saccades tends to values typical for fixation (microsaccades)
Saccades and microsaccades – the difference depends only on the stimulus (maybe physiologically these are the same)

## Slide 18: From exploration to fixation
Źródła: in. i Susanna Martinez-Conde From Exploration to Fixation: An Integrative View of Yarbus’s Vision Perception 44 (2015) 884-899
Jorge Otero-Millan, Stephen L. Macknik, Rachel E. Langston and Susana Martinez-Conde An oculomotor continuum from exploration to fixation PNAS 110 (2013) 6175-6180

## Slide 19
Stimulus

## Slide 20
Gaze positions

## Slide 21
Fixations and saccades / gaze path

## Slide 22
Fixations and saccades / gaze path

## Slide 23
Heat map

## Slide 24
Attention map

## Slide 25
Gaze position x and y coordinates

## Slide 26
Speed of gaze
Euler’s algorithm (simplest)

## Slide 27
Gaze acceleration
Euler’s algorithm (simplest)

## Slide 28
Events detection
Positional algorithm
Velocity algorithm
Fixation = group of samples for which
the position distribution is smaller
than the assumed threshold
Saccades = rest of samples
Fixation detection parameters:
- maximum dispersion in X / Y
- how to calculate the dispersion? (variance, maximum distances)
- minimum duration of fixation
- minimum number of samples during fixation
Saccade = a group of samples whose
speed is greater than the assumed
threshold
Fixations = rest of samples
Saccade detection:
- two- or three-point derivatives
- threshold speed or acceleration
- minimum speed at peak
- minimum duration
- minimum number of samples
- accuracy with which max speed is located at the center of the peak

## Slide 29
Velocity algorithm
time
speed
Condition 2:
peak wings
fall below
threshold speed
Condition 1:
exceeding the
minimum peak velocity
Condition 3: the minimum duration (number of samples)
Condition 4: peak at the center
Additionally: saccade may be
extended to some speed
Aim: saccades detection
Rest of the time: fixations

## Slide 30
Positional algorithm
Condition 1:
dispersion of a samples group
does not exceed the maximum
values (separately in X and Y)
Condition 2: minimum fixation duration
(or number of samples)
The method of dispersion calculating: variance or maximum distance of samples
ti
tf
Aim: fixations detection
Rest of the time: saccades

## Slide 31
Velocity algorithm
Events detection: blinking
Blink = quasi-fixation in zero position surrounded by two apparent saccades
Blink parameters:
- the minimum peak speed of both saccades
- minimum duration of quasi-fixation
- tolerance for a zero fixation position

## Slide 32
Events detection

## Slide 33
Events detection

## Slide 34
Events detection

## Slide 35
Smooth pursuit – „fixation on a moving object”
changing the gaze position in order to follow the object
usually impossible without the object (series of saccased)
speed lower than in case of saccades
If object is moving too fast (> 30°/s) smooth pursuit changes into a sequence of catch-up saccades
Smooth pursuit is physiologically different from the vestibular-ocular reflex
(the eye movement compensating the head movement during fixation).
Some people can start smooth running just imagining the moving object
Smooth is easier for objects moving horizontally than vertically (different brain areas are responsible)
Requires feedback with object (but continues while the object is for a moment covered). The first 100 ms - ballistic.
Events detection: smooth pursuit

## Slide 36
Areas of interests
1
2
3
4

## Slide 37
Total time spent in the AOI
Total time spent in the AOI per area field (normalized)
Total time spent in the AOI per total time for whole stimulus
Number of gazes in the AOI and number of returns to the AOI
Number of fixations in the AOI, percent of fixations in the AOI → interest in the detail/objects
Total duration of fixations in the AOI
Minimal, maximal and average duration of fixations in the AOI
Time to first fixation (TTFF) → visibility of the detail
Fixation dispersion
Area of interest (AOI)
Measures:
An area of any shape (usually a rectangle or an ellipse) surrounding possible
object of interest (e.g. advertising, dashboard element in the car, product, etc.)
Areas of interests

## Slide 38
Number of saccades to the AOI, number of saccades from the the AOI
Speed of these saccades
Transition matrix among the AOIs
Number of blinks in the AOI, frequency of blinks in the AOI
Minimal, maximal and average duration of the blinks in the AOI
Measures:
Areas of interests
Area of interest (AOI)
An area of any shape (usually a rectangle or an ellipse) surrounding possible
object of interest (e.g. advertising, dashboard element in the car, product, etc.)

## Slide 39
Gaze paths
Wikipedia
Ilya Repin Unexpected visitor (1884-1888), oil on canvas, 160 x 167 cm

## Slide 40
Gaze paths
Wikipedia
Ilya Repin Unexpected visitor (1884-1888), oil on canvas, 160 x 167 cm
Yarbus experiment (1967)
Lighting / color contrast

## Slide 41
Wikipedia
Gazes directions
Gaze paths
Ilya Repin Unexpected visitor (1884-1888), oil on canvas, 160 x 167 cm
Yarbus experiment (1967)

## Slide 42
Wikipedia
Gaze directions / relations / emotions
Gaze paths
Ilya Repin Unexpected visitor (1884-1888), oil on canvas, 160 x 167 cm
Yarbus experiment (1967)

## Slide 43
Wikipedia
Strong emotions, evolution
Gaze paths
Ilya Repin Unexpected visitor (1884-1888), oil on canvas, 160 x 167 cm
Yarbus experiment (1967)

## Slide 44
Wikipedia
Gaze paths
Ilya Repin Unexpected visitor (1884-1888), oil on canvas, 160 x 167 cm
Yarbus experiment (1967)

## Slide 45
Wikipedia
Gaze paths
Yarbus experiment (1967)

## Slide 46
Entropy (physics, thermodynamic) – measure of system disorder (randomness) and of energy dissipation, extensive function of the system state:
[J/K],
where k – Boltzmann constant, – number of possible microstates for energy E, - probability of i-th microstate
Entropy has maximal value if all microstates are equally probable (no information)
Entropy of information
C.E. Shannon A Mathematical Theory of Communication The Bell System Technical Journal 27 (1948) 379-423
Key concept of information theory (Claude Shanonn, 1948)
Entropy (information theory) – average amount of information for a single message
(weights are probabilities of message sending):
[bit]
Non-negative. The higher the value, the less we know about the microstate.

## Slide 47
bits
Transition matrix entropy
Let's assume three areas of interest marked with letters A, B and C.
An example of a normalized transition matrix between regions of interest R:
Transition matrix entropy:
[bit],
where ri – probability of gaze transition between two AOIs
Holmqvist i in. Eye Tracking: A Comprehensive Guide to Methods and Measures Oxford University Press 2011
Similar calculations can be made for time spend in AOIs, or even for a heat maps (answer to another question)
Value equal to zero (complete knowledge) - only in case of one AOI
Maximal value (no knowledge)
i.e. all probabilities are equal to 1/6.
H(R) = 2.59 bits
Normalized entropy (dimensionless) = entropy divided by maximal value
H = 2/2.59 = 77.2%

## Slide 48
Interpretation:
high values – exploration (transitions are equally probable), low values – more accurate examination of selected stimulus details (transitions occur only between selected areas, hence large differences in p(ri))
Holmqvist i in. Eye Tracking: A Comprehensive Guide to Methods and Measures Oxford University Press 2011
The value of entropy is sensitive to the choice of AOIs
Experiment: during free exploration of the stimulus: gradual decrease of the entropy value calculated for time intervals
(transition from exploration to examination of selected fragments/details)
Transition matrix entropy

## Slide 49
A well-known example of the use of entropy :
Shic i in. Eye Tracking: Autism, Eye-Tracking, Entropy 7th IEEE International Conference on Development and Learning (2008)
Shic, Chawarska, Scassellati (2008): different entropy values for healthy children
and children with ASD looking at the face image
2 i 4 y. old
avoidance…
Transition matrix entropy

## Slide 50: Software stack for ET
Software from ET manufacturer, third party’s or user designed
Eye tracker device and software delivered by its manufacturer
Pupils position detection
Determining the gaze position
Eye(s) images
real-time
offline
Simplified
event detection
Events analysis (fixations, saccades, blinks, ...)
Monitoring/Diagnosis/Experiments
feedback / ET as a controller
Game or experiment
25-2500 Hz

## Slide 51: Software stack for ET
Software from ET manufacturer, third party’s or user designed
Eye tracker device and software delivered by its manufacturer
Pupils position detection
Determining the gaze position
Eye(s) images
real-time
offline
GCAF
GIML
Gaze Data Explorer (GDE)
Monitoring/Diagnosis/Experiments
feedback / ET as a controller
GIML / GCAF
IEyetracker

## Slide 52: Software stack for ET
Software from ET manufacturer, third party’s or user designed
Eye tracker device and software delivered by its manufacturer
Pupils position detection
Determining the gaze position
Eye(s) images
real-time
offline
GCAF
GIML
Gaze Data Explorer (GDE)
Monitoring/Diagnosis/Experiments
feedback / ET as a controller
GIML / GCAF
IEyetracker